| Part No: 345879 (Type 1) Part number supercedes 330000 | Model: Series 2, 4 Cylinder | Dates of Use: March 1958 to December 1959 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Screw type vent controls | Early version has holes in PSK 3050 (Type 1A) | Pegasus 1st reference bulkhead = early parcel shelf stiffener |
| Lozenge holes for dip switch with rear wiring. | Later version has slots in PSK 3050 (Type 1B) |  |
| Bolt on door check tubes. | 2-litre and 2¼ models use different accelerator brackets |  |
| Angled tie bolt brackets. |  |  |
| RH Bonnet with locating lug. |  |  |
| Separate voltage regulator mounting plate. |  |  |
| Wiper motors fitted to windscreen. |  |  |
| Auxiliary panel for hand throttle, choke or engine stop and heater plug switch. |  |  |
| Round heater option. |  |  |
| No access hold for clutch slave cylinder bleed nipple. |  |  |
| Door hinges secured with 5/16” UNF square nuts welded to floating nut plate. |  |  |
| Return lip for windscreen seal. |  |  |
| Wings secured with 5/16” UNF square nuts held in special cages. |  |  |
| Plain Z-stiffener. |  |  |

| Part No: 345879 (Type 2) | Model: Series 2, 4 Cylinder | Dates of Use: January 1960 to c. May 1960 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Screw type vent controls. |  |  |
| Large round dipswitch with wiring to the side. (Principal change) |  |  |
| Bolt on door check tubes. |  |  |
| Angled tie bolt brackets. |  |  |
| RH Bonnet Hinge with locating lug. |  |  |
| Separate voltage regulator mounting plate. |  |  |
| Wiper motors fitted to windscreen. |  |  |
| Auxiliary panel for hand throttle, choke or engine stop and heater plug switch. |  |  |
| Round heater option. |  |  |
| Access hole for clutch slave cylinder bleed nipple. (Principle change) |  |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Return lip for windscreen seal. |  |  |
| Wings secured with Spire nuts. |  | 141001710 (January 1960) has Spire nuts to secure front wings. |

| Part No: 345879 (Type 3) | Model: Series 2, 4 Cylinder | Dates of Use: c. May 1960 to January 1962 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls (Principal Change). |  |  |
| Later type dipswitch. Wires to side. |  |  |
| Bolt on door check tubes. |  | 25100894A (Built 9th Jan 1962) |
| Separate voltage regulator mounting plate. |  |  |
| Wiper motors to windscreen. |  |  |
| Auxiliary panel for hand throttle, choke or engine stop and heater plug switch. |  |  |
| Round heater option. |  |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled tie bolt brackets. |  |  |
| RH Bonnet Hinge with locating lug. |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| Return lip for windscreen seal. |  |  |
| Wings secured with Spire nuts. |  |  |

| Part No: 345879 (Type 4) | Model: Series 2a, 4 Cylinder | Dates in Use: February 1962 to c. March 1967 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  | Fitted to chassis suffix ‘A’, ‘B’ and ‘C’. |
| Later type dipswitch. Wires to side. |  | Series 2a Forward Control. |
| Spot welded door check tubes. (Principal change) |  | Pegasus 3rd reference bulkhead built April 1965. |
| Voltage regulator mounted direct to bulkhead. |  |  |
| Wiper motors fitted to windscreen. |  |  |
| Auxiliary panel for hand throttle, choke or engine stop and heater plug switch. |  |  |
| Round heater option. |  |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled tie bolt brackets. |  | 25107914B has angled brackets. |
| RH Bonnet Hinge without locating lug. (Principal change?) |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| Return lip for windscreen seal. |  |  |
| Wings secured with Spire nuts. |  |  |
| Z-Stiffener has two raised stops. |  |  |

| Part No: 345879 (Type 5) | Model: Series 2a, 4 Cylinder | Dates of Use: c. March 1967 to October 1968 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  | Fitted to chassis suffix ‘D’ onwards. |
| Later type dipswitch. Wires to side. |  | 24134544D (Built 12th Sept 1968) |
| Spot welded door check tubes. |  | Series 2B Forward Control. |
| Voltage regulator mounted direct to bulkhead. |  |  |
| First type single wiper motor (LU DR3A) on left hand side, secured to LH side of glovebox. (Principal change) |  |  |
| Pressing in glovebox rear panel. (Principal change) |  |  |
| No auxiliary panel. |  |  |
| Horizontal type hand throttle mounted below instrument panel. |  |  |
| Round heater option. | Has demister holes for flat type heater. |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled tie bolt brackets. |  |  |
| RH Bonnet Hinge without locating lug. |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| No return lip for windscreen seal. ‘Archway’ press form to clear wiper motor spindles. |  |  |
| Wings secured with Spire nuts. |  |  |
| Holes in inner ventilator panel for washer jets only. |  |  |

| Part No: 345879 (Type 6) | Model: Series 2a, 4 Cylinder | Dates of Use: c. October 1968 to December 1968 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  |  |
| Later type dipswitch. Wires to side. |  |  |
| Spot welded door check tubes. |  |  |
| Voltage regulator mounted direct to bulkhead. |  |  |
| First type single wiper motor (LU DR3A) on left hand side, secured to LH side of glovebox. |  |  |
| Pressing in glovebox rear panel. |  |  |
| No auxiliary panel. |  |  |
| Horizontal type hand throttle mounted below instrument panel. |  |  |
| Flat heater option. (Principal change) | Holes for round heater demister tubes still present. |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled Tie Bolt brackets. |  |  |
| RH Bonnet Hinge without locating lug. |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| No return lip for windscreen seal. |  |  |
| Wings secured with Spire Nuts. |  |  |

| Part No: 345879 (Type 7) | Model: Series 2a, 4 Cylinder | Dates of Use: January 1969 to September 1969 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  | Fitted to chassis suffix ‘F’ onwards. |
| Later type dipswitch. Wires to side. |  |  |
| Spot welded door check tubes. |  |  |
| Voltage regulator mounted direct to bulkhead. |  |  |
| Second type single wiper motor (LU 75664) on left hand side, secured to front of glovebox. No pressing in glovebox rear panel. |  |  |
| No auxiliary panel. |  |  |
| Vertical hand throttle in glovebox. |  |  |
| Flat heater option. | Holes for round heater demister tubes still present. |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled Tie bolt brackets. |  |  |
| RH Bonnet Hinge without locating lug. |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| No return lip for windscreen seal. |  |  |
| Wings secured with Spire nuts. |  |  |

| Part No: 345879 (Type 8) | Model: Series 2a, 4 Cylinder | Dates of Use: October 1969 onwards |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  |  |
| Later type dipswitch. Wires to side. |  |  |
| Spot welded door check tubes. |  |  |
| Straight tie bolt brackets. (Principal change) |  |  |
| RH Bonnet Hinge without locating lug. |  |  |
| Voltage regulator mounted direct to bulkhead. |  |  |
| Second type single wiper motor (LU 75664) on left hand side, secured to front of glovebox. No pressing in glove box back panel. |  |  |
| No auxiliary panel. |  |  |
| Vertical hand throttle in glove box. |  |  |
| Flat heater option. | Holes for round heater demister tubes still present. |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| Wings secured with Spire nuts. |  |  |
| No return lip for windscreen seal. |  |  |
| Door hinges secured with Spire nuts. (Principal change) |  |  |

| Part No: 348500 | Model: Series 2a, 4 Cylinder, Rover 10/11, FFR | Dates of Use: 1967 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. |  | Pegasus reference bulkhead from 25113698D (07ET57) |
| Later type dipswitch. Wires to side. |  | Believed to be prototype for Type 6. |
| Spot welded door check tubes. |  |  |
| Voltage regulator mounted direct to bulkhead. |  |  |
| First type single wiper motor (LU DR3A) on left hand side, secured to LH side of glovebox. |  |  |
| Pressing in glovebox rear panel. |  |  |
| No auxiliary panel. |  |  |
| Horizontal type hand throttle mounted below instrument panel. |  |  |
| Middle panel punched for Round and Flat heaters. | Holes for round heater demister tubes still present. |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Angled Tie Bolt brackets. |  |  |
| RH Bonnet Hinge without locating lug. |  |  |
| Access hole for clutch slave cylinder bleed nipple. |  |  |
| No return lip for windscreen seal. |  |  |
| Inner Vent Panel with pilot holes for Fly Screens. |  |  |
| RH Footwell, LH Side Panel punched for Auxiliary Fuel Tank Switch-over Tap |  |  |
| Parcel shelf and Grab Handle drilled to accept Small Arms Clips. |  |  |
| Glove Box Back Panel with extra and larger holes for FFR cable ducting. |  |  |
| Wings secured with Spire Nuts. |  |  |

| Part No: 348571 | Model: Series 2a, NADA 6-Cylinder | Dates of Use: 1967 |
| --- | --- | --- |
| Main Features | Other Changes & Notes | Known Location/ Chassis No. |
| Quadrant type vent controls. | Reinforcement for bonnet hinge/tie bolt bracket is 5¼” wide. | Pegasus NADA reference bulkhead. Removed from 34300717A. |
| Later type dipswitch. Wires to side. | No holes for screenwash jets in outer ventilator panel. Present on inner clam. |  |
| Spot welded door check tubes. |  |  |
| Angled tie bolt brackets. |  |  |
| Voltage regulator mounted direct to bulkhead. |  |  |
| Single wiper motor (LU DR 3A) on left hand side, secured to LH side of glovebox. Pressing in glovebox rear panel. |  |  |
| Flat heater option. | Holes for round heater demister tubes still present. |  |
| Wings secured with Spire nuts. |  |  |
| Door hinges secured with 5/16” UNF square nuts attached to floating nut plates. |  |  |
| Right hand glovebox bottom panel, parcel shelf stiffener and parcel shelf z-piece modified for NADA demister tubes. |  |  |
| Right Hand Toe Panel is unique component to accept NADA heater. |  | NADA Heater Toe Panel = PSK 3227. |
| No return lip for windscreen seal. |  |  |